## Slide 1
Alt. Lost in Turn
Turn Diameter
Runway Length
Ground Roll
Glide Angle
Climb Angle
Alt. Power is Lost
Startle Duration and Shape
Transition from Turn to Glide
Final Turn to Align with Runway
Point towards Runway
Liftoff
Takeoff to Turnback Segments
Ground roll (distance)
Climb (angle)
Startle – (duration)
Turn (diameter and altitude loss)
Glide back (angle)
Final Turn to align with Runway (distance)
Engine Failure on Takeoff with Turnback
Climb Angle
A Segmented Analysis of the Maneuver
1. “We’ll reference this animation of a turnback trajectory that barely reaches a landing at the departure end of the takeoff runway. This will allow us to see how sensitive the result is to changing various parameters.
We’ve divided the trajectory into logical segments to break down our analysis. In sequence these are the ground roll, climb segment, the startle segment right after the failure, the turn maneuver, the glide back phase and a final turn to align with the runway”
Note – Narration text in black, video animation descriptions in blue
In sequence, flash each segment name while also flashing the segment stick on the diagram as the segment is named in the narration
Additional Turnback Factors
Runway Length
Altitude power is loss
Wind
2. “In addition to the flight path segments, there are three more factors to evaluate with the animation. These are the runway length, the altitude power is lost and the winds” Flash each box and the item on the diagram, as the names are pronounced
3. “The diagram shows a flight path scenario that just barely makes it back to the runway. The effects of varying each segment, as compared to this initial condition, will be shown in the following discussion.”
Flash a circle around the touchdown point as line 3 is narrated
Notes: If you then ask the question, how many of these turnback parts primarily depend on the design of the plane, you can see that quite a few do.
The best climb angle, the best glide angle, the ground roll, and the least altitude lost in even the best-flown turn all depend on the plane.
The rest depends on how the pilot flies the maneuver and how repeatable they can do it.
1 slide – Return Distance and Variability of the 34 planes
Surveyed over 1000 pilots – only 3% said that they could not make it back. 97% think that they could make it back to a 4000 ft runway from 600 to 800 feet.
We asked pilots across the US to record their own plane. We have flight recordings of over 30 types of planes with 150 attempts.
  Big differences between planes – Some never make it, some always, some in between
  Big variability in almost every pilot’s set of attempts. Without training you are probably just not precise enough predict what you next attempt will look like.
Three lessons learned
  Know Your Plane – Many planes struggle to make it, many make it easily. Unless you know your plane is capable of making it back (through our test protocol), don’t try it
  Know Yourself – Proficiency. Unless you have been trained to do the maneuver and are proficient with it, the odds of you performing the turnback in an emergency are against you.
    Aside: There are many videos of highly trained pilots in high performance planes showing you how you can do it. Ask yourself: do I have that type of plane? Am I as proficient as that pilot?
  Plan Ahead – The time to decide where you are going to point the plane is before you take off – startle time must be low

## Slide 2
Alt. Lost in Turn
Turn Diameter
Runway Length
Ground Roll
Glide Angle
Climb Angle
Alt. Power is Lost
Startle Duration and Shape
Transition from Turn to Glide
Final Turn to Align with Runway
Point towards Runway
Liftoff
Engine Failure on Takeoff with Turnback
Climb Angle
The Ground Roll Segment
1. “Looking first at the Ground Roll you’ll notice how a longer or shorter ground roll directly affects the final touchdown point…. assuming all other items remain unchanged. The longer ground roll proportionately moves the final touchdown point further away, while a shorter ground roll pulls the final touchdown point further into the runway.
Note – Narration text in black, video animation descriptions in blue
In animation, shift the liftoff point further down the runway, and move the entire remainder of the diagram to the right, driving the touchdown point off the end of the runway… then do the reverse, shifting the liftoff point to the left (shorter ground roll) and move the entire remainder of the diagram left, causing the touchdown to move left closer to the liftoff point.
2. “We know that ground roll changes with gross weight, density altitude, winds, runway surface and slope.
3. “Given this ground roll effect we should all question the wisdom of intersection takeoffs. Unless an intersection takeoff is required by the tower or for traffic, we should use the full runway.”
Notes: If you then ask the question, how many of these turnback parts primarily depend on the design of the plane, you can see that quite a few do.
The best climb angle, the best glide angle, the ground roll, and the least altitude lost in even the best-flown turn all depend on the plane.
The rest depends on how the pilot flies the maneuver and how repeatable they can do it.
1 slide – Return Distance and Variability of the 34 planes
Surveyed over 1000 pilots – only 3% said that they could not make it back. 97% think that they could make it back to a 4000 ft runway from 600 to 800 feet.
We asked pilots across the US to record their own plane. We have flight recordings of over 30 types of planes with 150 attempts.
  Big differences between planes – Some never make it, some always, some in between
  Big variability in almost every pilot’s set of attempts. Without training you are probably just not precise enough predict what you next attempt will look like.
Three lessons learned
  Know Your Plane – Many planes struggle to make it, many make it easily. Unless you know your plane is capable of making it back (through our test protocol), don’t try it
  Know Yourself – Proficiency. Unless you have been trained to do the maneuver and are proficient with it, the odds of you performing the turnback in an emergency are against you.
    Aside: There are many videos of highly trained pilots in high performance planes showing you how you can do it. Ask yourself: do I have that type of plane? Am I as proficient as that pilot?
  Plan Ahead – The time to decide where you are going to point the plane is before you take off – startle time must be low

## Slide 3
Alt. Lost in Turn
Turn Diameter
Runway Length
Ground Roll
Glide Angle
Climb Angle
Alt. Power is Lost
Startle Duration and Shape
Transition from Turn to Glide
Final Turn to Align with Runway
Point towards Runway
Liftoff
Engine Failure on Takeoff with Turnback
Climb Angle
Runway Length Effect
1. “Runway length has a similar effect. For identical conditions, the aircraft fails to return to a short runway but can make the longer runway with margin. It’s easy to see how use of intersection takeoffs effectively eliminates the advantage of longer runways in an emergency. The old saying applies; the two most useless things in aviation are the altitude above you and the runway behind you..”
Note – Narration text in black, video animation descriptions in blue
In animation, stretch the runway length well out to the right, making it about twice as long as shown… then retract it back to the left making it half as long as as shown. All the rest of the diagram does not move. As the narration begins to discuss the intersection takeoff, insert an intersection in the diagram and slide the entire stick diagram to the right showing the beginning of the takeoff roll is down at the intersection….
Intersecting taxiway
Notes: If you then ask the question, how many of these turnback parts primarily depend on the design of the plane, you can see that quite a few do.
The best climb angle, the best glide angle, the ground roll, and the least altitude lost in even the best-flown turn all depend on the plane.
The rest depends on how the pilot flies the maneuver and how repeatable they can do it.
1 slide – Return Distance and Variability of the 34 planes
Surveyed over 1000 pilots – only 3% said that they could not make it back. 97% think that they could make it back to a 4000 ft runway from 600 to 800 feet.
We asked pilots across the US to record their own plane. We have flight recordings of over 30 types of planes with 150 attempts.
  Big differences between planes – Some never make it, some always, some in between
  Big variability in almost every pilot’s set of attempts. Without training you are probably just not precise enough predict what you next attempt will look like.
Three lessons learned
  Know Your Plane – Many planes struggle to make it, many make it easily. Unless you know your plane is capable of making it back (through our test protocol), don’t try it
  Know Yourself – Proficiency. Unless you have been trained to do the maneuver and are proficient with it, the odds of you performing the turnback in an emergency are against you.
    Aside: There are many videos of highly trained pilots in high performance planes showing you how you can do it. Ask yourself: do I have that type of plane? Am I as proficient as that pilot?
  Plan Ahead – The time to decide where you are going to point the plane is before you take off – startle time must be low

## Slide 4
Alt. Lost in Turn
Turn Diameter
Runway Length
Ground Roll
Glide Angle
Climb Angle
Alt. Power is Lost
Startle Duration and Shape
Transition from Turn to Glide
Final Turn to Align with Runway
Point towards Runway
Liftoff
Engine Failure on Takeoff with Turnback
Climb Angle
The Climb Angle Segment
1. “The climb segment is a big contributor to the turnback result. Notice how increasing the climb angle raises all other subsequent points in the flight path and effectively keeps the aircraft closer to the runway as you climb. Also notice how the final touchdown point moves closer to the liftoff point as we increase the climb angle, while it moves further down range if we decrease the climb angle, all other factors remaining constant. In general, if the climb angle is not greater than the aircraft’s glidepath angle, the aircraft never gets above the glide plane and can’t make a turnback. The exception is for a very long runway where the aircraft may still be close enough after an engine failure to get back to the departure end.”
Note – Narration text in black, video animation descriptions in blue
In animation, steepen the climb angle segment while keeping all other segments fixed… this will raise the height of all points after the top of the climb… which will lengthen the glide angle leg before reaching the ground, and thus move the landing point closer to the liftoff point on the runway…. Next, shallow out the climb angle to show the reverse effect, resulting in a touchdown point short of the runway.
2. “Your climb angle will vary with gross weight, density altitude, winds, aircraft configuration and climb speed.
Your choice of Vx, Vy or a cruise climb speed is an often-debated topic. In general, it is best to use Vx only for clearing close in obstacles and use Vy to get to a safe altitude. Using a cruise climb immediately after departure can shrink your landing emergency options due to the shallower angle.
Raise/lower the climb angle and show how touchdown point moves left or right accordingly
Notes: If you then ask the question, how many of these turnback parts primarily depend on the design of the plane, you can see that quite a few do.
The best climb angle, the best glide angle, the ground roll, and the least altitude lost in even the best-flown turn all depend on the plane.
The rest depends on how the pilot flies the maneuver and how repeatable they can do it.
1 slide – Return Distance and Variability of the 34 planes
Surveyed over 1000 pilots – only 3% said that they could not make it back. 97% think that they could make it back to a 4000 ft runway from 600 to 800 feet.
We asked pilots across the US to record their own plane. We have flight recordings of over 30 types of planes with 150 attempts.
  Big differences between planes – Some never make it, some always, some in between
  Big variability in almost every pilot’s set of attempts. Without training you are probably just not precise enough predict what you next attempt will look like.
Three lessons learned
  Know Your Plane – Many planes struggle to make it, many make it easily. Unless you know your plane is capable of making it back (through our test protocol), don’t try it
  Know Yourself – Proficiency. Unless you have been trained to do the maneuver and are proficient with it, the odds of you performing the turnback in an emergency are against you.
    Aside: There are many videos of highly trained pilots in high performance planes showing you how you can do it. Ask yourself: do I have that type of plane? Am I as proficient as that pilot?
  Plan Ahead – The time to decide where you are going to point the plane is before you take off – startle time must be low

## Slide 5
Alt. Lost in Turn
Turn Diameter
Runway Length
Ground Roll
Glide Angle
Climb Angle
Alt. Power is Lost
Startle Duration and Shape
Transition from Turn to Glide
Final Turn to Align with Runway
Point towards Runway
Liftoff
Engine Failure on Takeoff with Turnback
Climb Angle
The Altitude Power is Lost
1. “The altitude power is lost tends to be the single parameter that pilots use when assessing whether to turn back. Many have a number of 800 feet in their hip pocket as the decision point for turnback. This unfortunately is a very unreliable parameter for decision making. The location of the aircraft relative to the runway when passing a target altitude can vary greatly with changing density altitude, gross weight and winds. Arriving at 800 feet AGL on one day could be coincident with the aircraft passing one mile off the end of the runway. Yet on a day with higher density altitude and higher gross weights, the aircraft might be nearly 2 miles from the runway when reaching 800 feet. The rest of the flight path would be dramatically different between these two situations. When someone asks what your turnback altitude is, your answer should be “that depends.” And it depends on each of the factors being demonstrated in this video.
Note – Narration text in black, video animation descriptions in blue
Move the point that shows altitude that power is lost away from the field and back towards the field, while leaving all other segments the same, to show how touchdown point moves left or right accordingly
Notes: If you then ask the question, how many of these turnback parts primarily depend on the design of the plane, you can see that quite a few do.
The best climb angle, the best glide angle, the ground roll, and the least altitude lost in even the best-flown turn all depend on the plane.
The rest depends on how the pilot flies the maneuver and how repeatable they can do it.
1 slide – Return Distance and Variability of the 34 planes
Surveyed over 1000 pilots – only 3% said that they could not make it back. 97% think that they could make it back to a 4000 ft runway from 600 to 800 feet.
We asked pilots across the US to record their own plane. We have flight recordings of over 30 types of planes with 150 attempts.
  Big differences between planes – Some never make it, some always, some in between
  Big variability in almost every pilot’s set of attempts. Without training you are probably just not precise enough predict what you next attempt will look like.
Three lessons learned
  Know Your Plane – Many planes struggle to make it, many make it easily. Unless you know your plane is capable of making it back (through our test protocol), don’t try it
  Know Yourself – Proficiency. Unless you have been trained to do the maneuver and are proficient with it, the odds of you performing the turnback in an emergency are against you.
    Aside: There are many videos of highly trained pilots in high performance planes showing you how you can do it. Ask yourself: do I have that type of plane? Am I as proficient as that pilot?
  Plan Ahead – The time to decide where you are going to point the plane is before you take off – startle time must be low

## Slide 6
Alt. Lost in Turn
Turn Diameter
Runway Length
Ground Roll
Glide Angle
Climb Angle
Alt. Power is Lost
Startle Duration and Shape
Transition from Turn to Glide
Final Turn to Align with Runway
Point towards Runway
Liftoff
Engine Failure on Takeoff with Turnback
Climb Angle
Startle Duration and Shape
1. “The startle upon experiencing an engine failure can dramatically affect the result. Fortunately, good training and consistent use of a pre-takeoff briefing can prepare you to make the correct response and minimize the startle effect. In simple terms, an aircraft climbing at 60 knots ground speed is moving away from the runway at one mile per minute. A ten second startle places the aircraft an additional 1,000 feet downrange from the runway as compared to an aircraft that begins the turn immediately. Also, if no action is taken to control the vertical flight path, the aircraft might be far off the target speed for the turn. Too fast results in excessive altitude loss, while failing to lower the nose to the proper power off glide angle could result in a stall.
Note – Narration text in black, video animation descriptions in blue
During the narration zoom in on this segment like below and show it stretching in animation to represent an extended startle and then show it shrink very small to reflect an immediate reaction with no startle delay. Similarly show the flight path descending and climbing above the turn arc to follow the narrative about the vertical flight path
Startle Duration and Shape
Notes: If you then ask the question, how many of these turnback parts primarily depend on the design of the plane, you can see that quite a few do.
The best climb angle, the best glide angle, the ground roll, and the least altitude lost in even the best-flown turn all depend on the plane.
The rest depends on how the pilot flies the maneuver and how repeatable they can do it.
1 slide – Return Distance and Variability of the 34 planes
Surveyed over 1000 pilots – only 3% said that they could not make it back. 97% think that they could make it back to a 4000 ft runway from 600 to 800 feet.
We asked pilots across the US to record their own plane. We have flight recordings of over 30 types of planes with 150 attempts.
  Big differences between planes – Some never make it, some always, some in between
  Big variability in almost every pilot’s set of attempts. Without training you are probably just not precise enough predict what you next attempt will look like.
Three lessons learned
  Know Your Plane – Many planes struggle to make it, many make it easily. Unless you know your plane is capable of making it back (through our test protocol), don’t try it
  Know Yourself – Proficiency. Unless you have been trained to do the maneuver and are proficient with it, the odds of you performing the turnback in an emergency are against you.
    Aside: There are many videos of highly trained pilots in high performance planes showing you how you can do it. Ask yourself: do I have that type of plane? Am I as proficient as that pilot?
  Plan Ahead – The time to decide where you are going to point the plane is before you take off – startle time must be low

## Slide 7
Engine Failure on Takeoff with Turnback
Climb Angle
The Turn – Diameter and Altitude Lost
“In the turning maneuver the objective is not maximum glide range but minimum altitude loss and minimum turn diameter, which requires slowest reasonable speed at the optimum bank. While turning it is critical to avoid stall. As the ground comes closer there can be a powerful incentive to pull back, which can induce a stall. Fly the proper attitude to maintain a safe stall margin. Mathematical analysis shows 45 degrees is the optimum bank angle. Targeting 35 – 45 degrees is good pilot technique. Less than 30 degrees results in a slow turn rate and the aircraft drifting down range while losing altitude. Greater than 50 degrees results in excessive sink and altitude loss while turning. Using the aircraft’s normal approach speed (Vref) provides sufficient stall margin at 45 degrees of bank, so Vref is a better speed than Vglide. You should train idle power steep turns at a safe altitude to gain proficiency in the maneuver.
Note – Narration text in black, video animation descriptions in blue
Alt. Lost in Turn
Turn Diameter
Runway Length
Ground Roll
Glide Angle
Climb Angle
Alt. Power is Lost
Startle Duration and Shape
Transition from Turn to Glide
Final Turn to Align with Runway
Point towards Runway
Liftoff
During the narration zoom in on this segment to show the effects described in 2.
2. Flying the turn too fast or at too shallow a bank results in the flight paths shown by the dashed lines. A shallow bank puts the aircraft further from the runway or excessive speed will finish the turn at a lower altitude.
Notes: If you then ask the question, how many of these turnback parts primarily depend on the design of the plane, you can see that quite a few do.
The best climb angle, the best glide angle, the ground roll, and the least altitude lost in even the best-flown turn all depend on the plane.
The rest depends on how the pilot flies the maneuver and how repeatable they can do it.
1 slide – Return Distance and Variability of the 34 planes
Surveyed over 1000 pilots – only 3% said that they could not make it back. 97% think that they could make it back to a 4000 ft runway from 600 to 800 feet.
We asked pilots across the US to record their own plane. We have flight recordings of over 30 types of planes with 150 attempts.
  Big differences between planes – Some never make it, some always, some in between
  Big variability in almost every pilot’s set of attempts. Without training you are probably just not precise enough predict what you next attempt will look like.
Three lessons learned
  Know Your Plane – Many planes struggle to make it, many make it easily. Unless you know your plane is capable of making it back (through our test protocol), don’t try it
  Know Yourself – Proficiency. Unless you have been trained to do the maneuver and are proficient with it, the odds of you performing the turnback in an emergency are against you.
    Aside: There are many videos of highly trained pilots in high performance planes showing you how you can do it. Ask yourself: do I have that type of plane? Am I as proficient as that pilot?
  Plan Ahead – The time to decide where you are going to point the plane is before you take off – startle time must be low

## Slide 8
Alt. Lost in Turn
Turn Diameter
Runway Length
Ground Roll
Glide Angle
Climb Angle
Alt. Power is Lost
Startle Duration and Shape
Transition from Turn to Glide
Final Turn to Align with Runway
Point towards Runway
Liftoff
Engine Failure on Takeoff with Turnback
Climb Angle
Glide Angle Segment
1. After completing the turn, target best glide speed to reach the runway. In some cases, the end of the turn might place the aircraft in a high energy situation where best glide may not be required. In that case, use a slip as appropriate and remember that flying faster or slower than Vglide will shorten the glide range. It is important to manage energy during the final portion of this leg to keep sufficient speed to flare without stalling. Use flaps as appropriate to reduce stall speed. Glide angles can typically be twice as steep engine out resulting in greater speed bleedoff in your flare as compared to normal powered approaches. Also be aware of the effect of a tailwind during this segment and the higher ground speeds approaching touchdown.
Note – Narration text in black, video animation descriptions in blue
During the narration show how the glide angle line steepens and comes up short for both a faster and slower speed than Vg. Increase the slope of the glide angle line to move the touchdown point to the right.
Notes: If you then ask the question, how many of these turnback parts primarily depend on the design of the plane, you can see that quite a few do.
The best climb angle, the best glide angle, the ground roll, and the least altitude lost in even the best-flown turn all depend on the plane.
The rest depends on how the pilot flies the maneuver and how repeatable they can do it.
1 slide – Return Distance and Variability of the 34 planes
Surveyed over 1000 pilots – only 3% said that they could not make it back. 97% think that they could make it back to a 4000 ft runway from 600 to 800 feet.
We asked pilots across the US to record their own plane. We have flight recordings of over 30 types of planes with 150 attempts.
  Big differences between planes – Some never make it, some always, some in between
  Big variability in almost every pilot’s set of attempts. Without training you are probably just not precise enough predict what you next attempt will look like.
Three lessons learned
  Know Your Plane – Many planes struggle to make it, many make it easily. Unless you know your plane is capable of making it back (through our test protocol), don’t try it
  Know Yourself – Proficiency. Unless you have been trained to do the maneuver and are proficient with it, the odds of you performing the turnback in an emergency are against you.
    Aside: There are many videos of highly trained pilots in high performance planes showing you how you can do it. Ask yourself: do I have that type of plane? Am I as proficient as that pilot?
  Plan Ahead – The time to decide where you are going to point the plane is before you take off – startle time must be low

## Slide 9
Alt. Lost in Turn
Turn Diameter
Runway Length
Ground Roll
Glide Angle
Climb Angle
Alt. Power is Lost
Startle Duration and Shape
Transition from Turn to Glide
Final Turn to Align with Runway
Point towards Runway
Liftoff
Engine Failure on Takeoff with Turnback
Climb Angle
Final Turn to Align with Runway
1. The turnback maneuver should not rollout on a base to an extended final but rather angled in at the end of the runway or at an achievable touchdown aimpoint down the runway. This minimizes the total distance flown. As seen in the overhead enlarged view on the right, the dashed line results in further distance traveled and less than optimum result. Also, from the geometry, it is obvious the maneuver is not a 180-degree turn, but closer to 210 - 240 degrees by aiming for the end of the runway. Turning along the dashed line flight path results in a 270-degree turn followed by a 90-degree turn (360 total) which results in much more energy loss. Such a turn could be appropriate in the case of a high energy situation at the end of the turnback.
Note – Narration text in black, video animation descriptions in blue
During the narration zoom from the view on the left to the view on the right.
Final Turn to Align with Runway
Notes: If you then ask the question, how many of these turnback parts primarily depend on the design of the plane, you can see that quite a few do.
The best climb angle, the best glide angle, the ground roll, and the least altitude lost in even the best-flown turn all depend on the plane.
The rest depends on how the pilot flies the maneuver and how repeatable they can do it.
1 slide – Return Distance and Variability of the 34 planes
Surveyed over 1000 pilots – only 3% said that they could not make it back. 97% think that they could make it back to a 4000 ft runway from 600 to 800 feet.
We asked pilots across the US to record their own plane. We have flight recordings of over 30 types of planes with 150 attempts.
  Big differences between planes – Some never make it, some always, some in between
  Big variability in almost every pilot’s set of attempts. Without training you are probably just not precise enough predict what you next attempt will look like.
Three lessons learned
  Know Your Plane – Many planes struggle to make it, many make it easily. Unless you know your plane is capable of making it back (through our test protocol), don’t try it
  Know Yourself – Proficiency. Unless you have been trained to do the maneuver and are proficient with it, the odds of you performing the turnback in an emergency are against you.
    Aside: There are many videos of highly trained pilots in high performance planes showing you how you can do it. Ask yourself: do I have that type of plane? Am I as proficient as that pilot?
  Plan Ahead – The time to decide where you are going to point the plane is before you take off – startle time must be low

## Slide 10
Alt. Lost in Turn
Turn Diameter
Runway Length
Ground Roll
Glide Angle
Climb Angle
Alt. Power is Lost
Startle Duration and Shape
Transition from Turn to Glide
Final Turn to Align with Runway
Point towards Runway
Liftoff
Engine Failure on Takeoff with Turnback
Climb Angle
Final Turn to Align with Runway
1. A final important consideration is the wind condition on takeoff. A strong headwind will keep the aircraft closer to the end of the runway during climb due to the slower ground speed. This effectively increases the climb angle which is a beneficial effect. In the event of quartering or direct crosswinds, you should note that turning into the wind will shorten the radius of a turnback while an initial turn downwind will widen the radius and increase the distance that has to be flown. A turnback may be achievable into a crosswind but not possible if the turn is initiated downwind.
Note – Narration text in black, video animation descriptions in blue
During the narration zoom from the view on the left to the view on the right.
Headwind Turn
Wind direction
Downwind turn
Notes: If you then ask the question, how many of these turnback parts primarily depend on the design of the plane, you can see that quite a few do.
The best climb angle, the best glide angle, the ground roll, and the least altitude lost in even the best-flown turn all depend on the plane.
The rest depends on how the pilot flies the maneuver and how repeatable they can do it.
1 slide – Return Distance and Variability of the 34 planes
Surveyed over 1000 pilots – only 3% said that they could not make it back. 97% think that they could make it back to a 4000 ft runway from 600 to 800 feet.
We asked pilots across the US to record their own plane. We have flight recordings of over 30 types of planes with 150 attempts.
  Big differences between planes – Some never make it, some always, some in between
  Big variability in almost every pilot’s set of attempts. Without training you are probably just not precise enough predict what you next attempt will look like.
Three lessons learned
  Know Your Plane – Many planes struggle to make it, many make it easily. Unless you know your plane is capable of making it back (through our test protocol), don’t try it
  Know Yourself – Proficiency. Unless you have been trained to do the maneuver and are proficient with it, the odds of you performing the turnback in an emergency are against you.
    Aside: There are many videos of highly trained pilots in high performance planes showing you how you can do it. Ask yourself: do I have that type of plane? Am I as proficient as that pilot?
  Plan Ahead – The time to decide where you are going to point the plane is before you take off – startle time must be low